https://www.cscs.ch/computers/piz-daint/
https://www.top500.org/system/178451
Specifications:
- Piz Daint is used for high-resolution simulations and in data science to analyse large volumes of data.
- Located at Swiss National Supercomputing Centre
- Cray XC40/XC50 system with 5704 XC50 nodes and 1813 XC40 nodes

- XC50 System:
  - Each XC50 node has:
    - One 12-core Intel Xeon E5-2690 v3 CPUs with 64 GB Ram
    - One NVIDIA Tesla P100 ([4]Pascal-based GPU) with 16 GB
  - Max Achieved Performance(Rmax): 21230 TFlop/s
  - Max Theoretical Performance(Rpeak): 27154.3 TFlop/s
  - Power Consumption: 2384.24 kW
  - 387872 Cores
  - 365056 GB memory
- XC40 System:
  - Each XC40 node has:
    - Two 18-core Intel Xeon E5-2695 v4 CPUs with 64/128 GB RAM
  - Max Achieved Performance(Rmax): 1896.75 TFlop/s
  - Max Theoretical Performance(Rpeak): 2193.01 TFlop/s
  - Power Consumption: 732.40 kW
  - 65268 Cores
  - 116032 GB memory
- Interconnect Configuration with Aries routing and communications ASIC, and Dragonfly network topology

CPU:
https://ark.intel.com/content/www/us/en/ark/products/91316/intel-xeon-processor-e5-2695-v4-45m-cache-2-10-ghz.html [8]
- Intel Xeon E5-2695 v4
  - Contains 18 cores, each of which can process up to 36 threads
  - Has 45 MB Cache memory
  - Max Memory Size of 1.5TB
  - 4 Memory Channels
  - Max Memory Bandwidth: 46-bit/s
https://ark.intel.com/content/www/us/en/ark/products/81713/intel-xeon-processor-e5-2690-v3-30m-cache-2-60-ghz.html [9]
- Intel Xeon E5-2690 v3
  - Contains 12 cores, each of which can process up to 24 threads
  - Has 30 MB Cache memory
  - Max Memory Size of 768GB
  - 4 Memory Channels
  - Max Memory Bandwidth: 68-bit/s
- Both of these utilize Intel Hyper-Threading Technology with Turbo Boost (see [10],[11])
- Both have Intel Virtualization Technology (see[12])

https://www.intel.com/content/www/us/en/architecture-and-technology/hyper-threading/hyper-threading-technology.html [10]
- Intel Hyper Threading Technology
  - Utilizes processor resources more efficiently to allow multiple threads to run on each core
  - It also dynamically adapts to workload and automatically disables inactive cores, which increases processor frequency on busy cores, giving a bigger performance boost.
https://www.intel.com/content/www/us/en/architecture-and-technology/turbo-boost/turbo-boost-technology.html [11]
- Intel Turbo Boost Technology
  - When a processor is running below its operational limit, the user choose to boost the processor frequency until it hits its limit.
  - Utilizes parallel algorithms to manage power, current, and temperature to manage the frequency to energy consumption ration.

https://www.hardwaresecrets.com/everything-you-need-to-know-about-the-intel-virtualization-technology/
https://www.intel.com/content/www/us/en/virtualization/virtualization-technology/intel-virtualization-technology.html [12]
- Intel Virtualization Technology
  - Allows the CPU to create multiple virtual CPUs, each with their own OS, and run applications on all of them simultaneously.
  - Faithful abstraction means no performance or compatibility loss, as if running on a dedicated CPU
  - Memory virtualization allows abstraction to isolate memory for each virtual CPU, this assists in VM migrations and fault detection/tolerance.

GPU:
https://www.nvidia.com/content/dam/en-zz/Solutions/Data-Center/tesla-p100/pdf/nvidia-tesla-p100-datasheet.pdf
https://nvidianews.nvidia.com/news/nvidia-pascal-gpus-to-double-speed-of-europe-s-fastest-supercomputer
https://images.nvidia.com/content/pdf/tesla/whitepaper/pascal-architecture-whitepaper.pdf
(This last url is pretty in depth)
[13]
- NVIDIA Tesla P100
  - Utilizes a Pascal GP100 architecture, replacing the Maxwell architecture
    - Pascal GPUs feature a number of breakthrough technologies, including second-generation High Bandwidth Memory (HBM2) that delivers three times higher bandwidth than the previous generation architecture, and 16nm FinFET technology for unprecedented energy efficiency
  - 3584 CUDA Cores
  - Uses HBM2 (High Bandwidth Memory)
  - 16 GB of HBM2 stacked memory
  - 4096 KB L2 Cache
  - 15.3 billion transistors
  - Features NVIDIA NVLink™ technology

https://www.cscs.ch/publications/fact-sheets/piz-daint-one-of-the-most-powerful-supercomputers-in-the-world/ [3]
https://www.cscs.ch/publications/press-releases/2016/more-computing-power-for-swiss-research/ [4]
https://insidehpc.com/2016/08/creating-balance-in-hpc/ [5]
https://www.cray.com/sites/default/files/resources/CrayXC40-DataWarp.pdf [6]
https://www.youtube.com/watch?v=3HDBEO8lO5M [7]
Parallelization:
[3]Piz Daint can scale simulations and data analysis algorithms to thousands of nodes

- [5]As supercomputers continue to scale they face increasing challenges around memory bandwidth. To combat this, Piz Daint utilizes a CrayXC40 DataWarp
  - [5][7] DataWarp is an IO accelerator that uses SSDs to reduce bottlenecks between GPU and CPU, as well as help bridge the gap between storage and compute performance.
  - [6] Datawarp can be used as a storage cache for parallel file systems(PFS).
    - [6] This absorbs any possible I/O spikes to keep the storage cost down
    - Improves the utilization of parallel file systems by buffering performance across the files
    - Improves overall application performance by decoupling application I/O from PFS I/O
  - “Burst buffer mode” quadruples effective bandwidth to and from long term storage devices.
    - Greatly increases data input and output rate
    - Allows for analysis on millions of small unstructured files
    - [4]Allows Piz Daint to transfer initial results of calculations to a specialized area for analysis while continuing to run calculations